## Slide 1: FAST MESSAGE PROPAGATION OVER IOV SCENARIOS
Dipartimento di Matematica "Tullio Levi-Civita"
Laurea in Informatica
a.a. 2018-2019
Jordan Gottardo 1179739
Esame di laurea - 18 Luglio 2019
1/14
Relatore: Prof. Claudio Enrico Palazzi
Co-relatore: Dott. Armir Bujari

## Slide 2: CONTENTS
Context
Simulations
Conclusions
Context
Technologies
My contributions
Scenarios
Metrics
Simulation results
Algorithm extensions
Extension evaluation
Conclusions
State of the art
Future works

## Slide 3
Intro
Contents
Context 1: IOV scenarios VANET, DANET, ESD
Context 2 / Technologies, ns-3, obstacle model forse estendere a 2 slides
Miei contributi
Algorithm 1: Fast-Broadcast
Algorithm 2: ROFF
Qualitative: buildings no buildings fb roff ecc
Lista scenari: Platoon 1D, Grid 2D, LA, Padova, LA smart city
Scenario 3D varie distanze
5 metriche
Scenario: Padova no SJ
  5 metriche no buildings + buildings
Smart Junction extension
Scenario: Padova con SJ
  5 metriche buildings no SJ + buildings SJ
Scenario 2: LA Smart City 2D + 3D
  5 metriche no build + build + high build? Se ci stanno tutti e 3
Scenario forging attack
Conclusioni

## Slide 4: CONTEXT
5
Vehicular and Flying Ad-Hoc Networks (VANETs and FANETs)
Several applications
  Smart city management
  Video streaming
  Traffic control
Focus: Emergency Message Distribution (EMD)
  Message delivery
  Timeliness
  Avoid medium saturation

## Slide 5: TECHNOLOGIES AND TOOLS
5
Expensive large scale tests
  Need to use simulators (ns-3)
Additional tools and models
  Real map data
  Road junction modeling
Signal propagation models
  Two-Ray Ground
  Obstacle shadowing (with 3D extension) [1] [2]
[1] C. Sommer, D. Eckhoff, R. German, and F. Dressler, “A computationally inexpensive empirical model of ieee 802.11p radio shadowing in urban environments”, 2011
[2] M. Romanelli, C. Palazzi, and A. Bujari, “Propagazione di messaggi tra veicoli con modello urbano realistico”, Master’s thesis, University of Padua, 2017.

## Slide 6: FAST-BROADCAST
5
Multi-hop probabilistic delay-based broadcasting protocol
Dynamic transmission range estimation
  No need to know it a priori, as often assumed in other protocols
Estimation Phase:
  Vehicles exchange small Hello Messages (beacons) to estimate their transmission range
  1 Hello Message sent every turn within each transmission range
Broadcast Phase:
  A vehicle sends an Alert Message
  The neighbors receive it and participate in contention to broadcast it
  The vehicles farther from sender wait less time before broadcast
  Waiting time depends directly on sender-receiver distance

## Slide 7: ROFF (RObust Fast Forwarding)
5
Multi-hop deterministic delay-based broadcasting protocol
Deterministically determines the farthest forwarder
Estimation Phase:
  Each vehicle sends a Hello Message every BeaconInterval (e.g., 100ms)
  Neighborhood discovery process
  Each vehicle builds a Neighbor Table (NBT) with one entry for each neighbor
Broadcast Phase:
  Waiting time differentiation based on unique forwarding priority
  Vehicles estimate their own priority
  High priority = low waiting time
  No direct dependency on sender-receiver distance

## Slide 8: MY CONTRIBUTIONS
5
Improvements to Fast-Broadcast
Implementation and extension to 2D and 3D scenarios of ROFF
Evaluation and comparison of Fast-Broadcast and ROFF through simulations
  Urban scenarios with and without buildings
Proposal of extension to exploit road junctions to increase message delivery ratios
  SJ-Fast-Broadcast and SJ-ROFF (SJ=Smart Junction)

## Slide 9: SIMULATIONS – SCENARIOS AND METRICS
5
Several scenarios of increasing complexity
Scenario name | Type | Buildings | Drones
Platoon | 1D |  | 
Grid | 2D |  | 
Los Angeles | 2D |  | 
Padua | 2D |  | 
Los Angeles smart city | 3D |  | 
Metrics
  Total delivery ratio
  Total delivery ratio on circumference
  Number of hops
  Number of slots
  Forwarding node number
  }
Coverage
  }
End-to-end delay
  }
Redundancy

## Slide 10: URBAN SCENARIOS
5
Los Angeles
Padua

## Slide 11: PRELIMINARY TESTS
5
Scenario configuration | 
Scenario name | Padua
Latitude N [°] | 45.4171
Latitude S [°] | 45.3981
Longitude W [°] | 11.8654
Longitude E [°] | 11.8923
Circumference radius [m] | 1000
Distance between vehicles [m] | 5, 15, 25, 35, 45
Number of vehicles | 4975, 2856, 1775, 1318, 1072
Number of simulations | 4500
Simulator configuration | 
Packet payload size | 100 byte
Frequency [GHz] | 2.4
Channel bandwidth [MHz] | 22
Transmission speed [Mbps] | 11
Transmission powers [dBm] | -7.0, 4.6, 13.4
Transmission ranges [m] | 100, 300, 500
Modulation | DSSS
Propagation loss model | ns3::TwoRayGround
Propagation delay model | ns3::ConstantSpeed

## Slide 12: PRELIMINARY TESTS - DELIVERY RATIOS
5

## Slide 13: PRELIMINARY TESTS – NUMBER OF HOPS
5

## Slide 14: PRELIMINARY TESTS – NUMBER OF SLOTS
5

## Slide 15: FORWARDING NODE NUMBER
5

## Slide 16: PADUA URBAN SCENARIO
5
Scenario configuration | 
Scenario name | Padua
Latitude N [°] | 45.4171
Latitude S [°] | 45.3981
Longitude W [°] | 11.8654
Longitude E [°] | 11.8923
Circumference radius [m] | 1000
Distance between vehicles [m] | 25
Number of vehicles | 1775
Number of buildings | 6322
Number of simulations | 4500
Simulator configuration | 
Packet payload size | 100 byte
Frequency [GHz] | 2.4
Channel bandwidth [MHz] | 22
Transmission speed [Mbps] | 11
Transmission powers [dBm] | -7.0, 4.6, 13.4
Transmission ranges [m] | 100, 300, 500
Modulation | DSSS
Propagation loss model | ns3::TwoRayGround
Propagation delay model | ns3::ConstantSpeed
Shadowing model | ns3::ObstacleShadowing

## Slide 17
5
Without buildings
With buildings
PADUA – TOTAL DELIVERY RATIO

## Slide 18
5
Without buildings
With buildings
PADUA – TOTAL DELIVERY RATIO ON CIRC.

## Slide 19
5
JUNCTION MODEL
Aim: exploit vehicles located within junctions to improve delivery ratios
Identification of junctions via OSM/SUMO tools
20x20m bounding box to extend the polygon
Vehicles within a junction participate in a second contention with other vehicles within the same junction
Extension applicable both to Fast-Broadcast and ROFF
  SJ-Fast-Broadcast and SJ-ROFF

## Slide 20
5
JUNCTION MODEL - EXAMPLE
Without junction model
With junction model

## Slide 21
5
JUNCTION MODEL - SCENARIOS
Los Angeles
Padua

## Slide 22: PADUA URBAN SCENARIO WITH JUNCTIONS
5
Scenario configuration | 
Scenario name | Padua
Latitude N [°] | 45.4171
Latitude S [°] | 45.3981
Longitude W [°] | 11.8654
Longitude E [°] | 11.8923
Circumference radius [m] | 1000
Distance between vehicles [m] | 25
Number of vehicles | 1775
Number of buildings | 6322
Number of junctions | 3231
Number of simulations | 4500
Simulator configuration | 
Packet payload size | 100 byte
Frequency [GHz] | 2.4
Channel bandwidth [MHz] | 22
Transmission speed [Mbps] | 11
Transmission powers [dBm] | -7.0, 4.6, 13.4
Transmission ranges [m] | 100, 300, 500
Modulation | DSSS
Propagation loss model | ns3::TwoRayGround
Propagation delay model | ns3::ConstantSpeed
Shadowing model | ns3::ObstacleShadowing

## Slide 23
5
With buildings, without junctions
PADUA – TOTAL DELIVERY RATIO
With buildings, with junctions

## Slide 24
5
With buildings, without junctions
PADUA – TOTAL DELIVERY RATIO ON CIRC.
With buildings, with junctions

## Slide 25
5
With buildings, without junctions
PADUA – NUMBER OF HOPS
With buildings, with junctions

## Slide 26
5
With buildings, without junctions
PADUA – NUMBER OF SLOTS
With buildings, with junctions

## Slide 27
5
With buildings, without junctions
PADUA – FORWARDING NODE NUMBER
With buildings, with junctions

## Slide 28
5
L.A. SMART CITY SCENARIO
Vehicular + drones mixed scenario
  Message propagation in 3D
Different buildings configurations
  No buildings

## Slide 29
5
L.A. SMART CITY SCENARIO
Vehicular + drones mixed scenario
  Message propagation in 3D
Different buildings configurations
  No buildings
  Buildings with real heights

## Slide 30
5
L.A. SMART CITY SCENARIO
Vehicular + drones mixed scenario
  Message propagation in 3D
Different buildings configurations
  No buildings
  Buildings with real heights
  Very tall buildings

## Slide 31
5
LOS ANGELES – TOTAL DELIVERY RATIO

## Slide 32
5
CONCLUSIONS
ROFF introduces a much smaller end-to-end delay (number of slots) than Fast-Broadcast
  Greater forwarding number
  Determinism and collisions
  Number of Hello Messages
SJ-Fast-Broadcast and SJ-ROFF improve delivery ratios greatly
  At the cost of more retransmissions
The algorithms work well even in mixed 3D scenarios

## Slide 33
5
FUTURE WORKS
Dynamic lower and upper bounds for Fast-Broadcast’s waiting time calculation
  Based on vehicle density
Junction identification backup mode
  Reliance on GPS
  Compute angle between received messages to identify vehicles within junctions
Evaluation in more widespread FANETs