## Slide 1
Università degli Studi di Padova Dipartimento di Matematica "Tullio Levi-Civita"
Laurea Magistrale in Informatica
a.a. 2018-2019
Jordan Gottardo 1179739
Esame di laurea - 18 Luglio 2019
Relatore: Prof. Claudio Enrico Palazzi
Co-relatore: Dott. Armir Bujari
FAST MESSAGE PROPAGATION OVER IOV SCENARIOS
1

## Slide 2: CONTENTS
Context
Simulations
Conclusions
Context
Technologies
My contributions
Scenarios
Metrics
Simulation results
Algorithm extensions
Extension evaluation
Conclusions
State of the art
Future works
2

## Slide 3: CONTEXT
Vehicular and Flying Ad-Hoc Networks (VANETs and FANETs)
Several applications
  Smart city management
  Video streaming
  Traffic control
Focus: Emergency Message Distribution (EMD)
  Message delivery
  Timeliness
  Avoid medium saturation
3

## Slide 4: TECHNOLOGIES AND TOOLS
Expensive large scale tests
  Need to use simulators (ns-3)
Additional tools and models
  Real map data
  Road junction modeling
Signal propagation models
  Two-Ray Ground
  Obstacle shadowing (with 3D extension)
4

## Slide 5: FAST-BROADCAST
Multi-hop probabilistic delay-based broadcasting protocol
Dynamic transmission range estimation
  No need to know it a priori, as often assumed in other protocols
Estimation Phase:
  Vehicles exchange small Hello Messages (beacons) to estimate their transmission range
  1 Hello Message sent every BeaconInterval (e.g., 100ms) within each transmission range
Broadcast Phase:
A
B
C
D
Waiting time | [0…1024] | [0…512] | [0…32]
5

## Slide 6: ROFF (RObust Fast Forwarding)
Multi-hop deterministic delay-based broadcasting protocol
Deterministically defines the farthest forwarder
Estimation Phase:
  Each vehicle sends a Hello Message every BeaconInterval (e.g., 100ms)
  Neighborhood discovery process
  Each vehicle builds a Neighbor Table (NBT) with one entry for each neighbor
Broadcast Phase:
A
B
C
D
Priority | 3 | 2 | 1
Waiting time | 2 | 1 | 0
6

## Slide 7: MY CONTRIBUTIONS
Improvements to Fast-Broadcast
Implementation and extension to 2D and 3D scenarios of ROFF
Evaluation and comparison of Fast-Broadcast and ROFF through simulations
  Urban scenarios with and without buildings
Proposal of extension to exploit road junctions to increase message delivery ratios
  SJ-Fast-Broadcast and SJ-ROFF (SJ=Smart Junction)
7

## Slide 8: SIMULATIONS – SCENARIOS AND METRICS
Several scenarios of increasing complexity
Scenario name | Type | Buildings | Drones
Platoon | 1D |  | 
Grid | 2D |  | 
Los Angeles | 2D |  | 
Padua | 2D |  | 
Los Angeles smart city | 3D |  | 
Metrics:
  Coverage ↑
  End-to-end delay ↓
  Redundancy ↓
8

## Slide 9: URBAN SCENARIOS
Los Angeles
Padua
9

## Slide 10: PRELIMINARY TESTS - CONFIGURATION
Scenario configuration | 
Scenario name | Padua
Latitude N [°] | 45.4171
Latitude S [°] | 45.3981
Longitude W [°] | 11.8654
Longitude E [°] | 11.8923
Circumference radius [m] | 1000
Distance between vehicles [m] | 5, 15, 25, 35, 45
Number of vehicles | 4975, 2856, 1775, 1318, 1072
Number of simulations | 4500
Simulator configuration | 
Packet payload size | 100 byte
Frequency [GHz] | 2.4
Channel bandwidth [MHz] | 22
Transmission speed [Mbps] | 11
Transmission powers [dBm] | -7.0, 4.6, 13.4
Transmission ranges [m] | 100, 300, 500
Modulation | DSSS
Propagation loss model | ns3::TwoRayGround
Propagation delay model | ns3::ConstantSpeed
10

## Slide 11: END-TO-END DELAY ↓
↑ Coverage: comparable results
↓ End-to-end delay:
11

## Slide 12: REDUNDANCY ↓
12

## Slide 13: PADUA URBAN SCENARIO
Scenario configuration | 
Scenario name | Padua
Latitude N [°] | 45.4171
Latitude S [°] | 45.3981
Longitude W [°] | 11.8654
Longitude E [°] | 11.8923
Circumference radius [m] | 1000
Distance between vehicles [m] | 25
Number of vehicles | 1775
Number of buildings | 6322
Number of simulations | 4500
Simulator configuration | 
Packet payload size | 100 byte
Frequency [GHz] | 2.4
Channel bandwidth [MHz] | 22
Transmission speed [Mbps] | 11
Transmission powers [dBm] | -7.0, 4.6, 13.4
Transmission ranges [m] | 100, 300, 500
Modulation | DSSS
Propagation loss model | ns3::TwoRayGround
Propagation delay model | ns3::ConstantSpeed
Shadowing model | ns3::ObstacleShadowing
13

## Slide 14
Without buildings
With buildings
PADUA – COVERAGE ↑
14

## Slide 15
EXPLOITING JUNCTIONS – EXAMPLE
Without junction model
With junction model
15

## Slide 16
JUNCTION MODEL
Aim: exploit vehicles located within junctions to improve coverage
Identification of junctions via OSM/SUMO tools
20x20m bounding box to extend the polygon
Vehicles within a junction participate in a second contention with other vehicles within the same junction
Extension applicable both to Fast-Broadcast and ROFF
  SJ-Fast-Broadcast and SJ-ROFF
16

## Slide 17
JUNCTION MODEL - SCENARIOS
Los Angeles
Padua
17

## Slide 18: PADUA URBAN SCENARIO WITH JUNCTIONS
Scenario configuration | 
Scenario name | Padua
Latitude N [°] | 45.4171
Latitude S [°] | 45.3981
Longitude W [°] | 11.8654
Longitude E [°] | 11.8923
Circumference radius [m] | 1000
Distance between vehicles [m] | 25
Number of vehicles | 1775
Number of buildings | 6322
Number of junctions | 3231
Number of simulations | 4500
Simulator configuration | 
Packet payload size | 100 byte
Frequency [GHz] | 2.4
Channel bandwidth [MHz] | 22
Transmission speed [Mbps] | 11
Transmission powers [dBm] | -7.0, 4.6, 13.4
Transmission ranges [m] | 100, 300, 500
Modulation | DSSS
Propagation loss model | ns3::TwoRayGround
Propagation delay model | ns3::ConstantSpeed
Shadowing model | ns3::ObstacleShadowing
18

## Slide 19
Without junctions
PADUA – COVERAGE ↑
With junctions
19

## Slide 20
PADUA – REDUNDANCY ↓
Without junctions
With junctions
20

## Slide 21
L.A. SMART CITY SCENARIO
Vehicular + drones mixed scenario
  Message propagation in 3D
Different buildings configurations
  No buildings
21

## Slide 22
L.A. SMART CITY SCENARIO
Vehicular + drones mixed scenario
  Message propagation in 3D
Different buildings configurations
  No buildings
  Buildings with real heights
21

## Slide 23
L.A. SMART CITY SCENARIO
Vehicular + drones mixed scenario
  Message propagation in 3D
Different buildings configurations
  No buildings
  Buildings with real heights
  Very tall buildings
21

## Slide 24
LOS ANGELES – COVERAGE ↑
Without buildings
Real height buildings
Very tall buildings
22

## Slide 25
CONCLUSIONS
ROFF introduces a much smaller end-to-end delay than Fast-Broadcast
  Greater redundancy
  Determinism and collisions
  High number of Hello Messages
SJ-Fast-Broadcast and SJ-ROFF improve coverage greatly
  At the cost of more retransmissions
The algorithms work well even in mixed 3D scenarios
23

## Slide 26
FUTURE WORKS
Dynamic lower and upper bounds for Fast-Broadcast’s waiting time calculation
  Based on vehicle density
Junction identification backup mode
  Reliance on GPS
  Compute angle between received messages to identify vehicles within junctions
Evaluation in more widespread FANETs
24

## Slide 27: FAST-BROADCAST
5
Multi-hop probabilistic delay-based broadcasting protocol
Dynamic transmission range estimation
  No need to know it a priori, as often assumed in other protocols
Estimation Phase:
  Vehicles exchange small Hello Messages (beacons) to estimate their transmission range
  1 Hello Message sent every turn within each transmission range
Broadcast Phase:
  A vehicle sends an Alert Message
  The neighbors receive it and participate in contention to broadcast it
  The vehicles farther from sender wait less time before broadcast
  Waiting time depends directly on sender-receiver distance

## Slide 28: ROFF (RObust Fast Forwarding)
5
Multi-hop deterministic delay-based broadcasting protocol
Deterministically determines the farthest forwarder
Estimation Phase:
  Each vehicle sends a Hello Message every BeaconInterval (e.g., 100ms)
  Neighborhood discovery process
  Each vehicle builds a Neighbor Table (NBT) with one entry for each neighbor
Broadcast Phase:
  Waiting time differentiation based on unique forwarding priority
  Vehicles estimate their own priority
  High priority = low waiting time
  No direct dependency on sender-receiver distance

## Slide 29: SIMULATIONS – SCENARIOS AND METRICS
5
Several scenarios of increasing complexity
Scenario name | Type | Buildings | Drones
Platoon | 1D |  | 
Grid | 2D |  | 
Los Angeles | 2D |  | 
Padua | 2D |  | 
Los Angeles smart city | 3D |  | 
Metrics:
  Total delivery ratio
  Total delivery ratio on circumference
  Number of hops
  Number of slots
  Forwarding node number
  }
Coverage
  }
End-to-end delay
  }
Redundancy

## Slide 30: PRELIMINARY TESTS - DELIVERY RATIOS
5

## Slide 31: PRELIMINARY TESTS – NUMBER OF HOPS
5

## Slide 32
5
Without buildings
With buildings
PADUA – TOTAL DELIVERY RATIO ON CIRC.

## Slide 33
5
With buildings, without junctions
PADUA – TOTAL DELIVERY RATIO ON CIRC.
With buildings, with junctions

## Slide 34
5
With buildings, without junctions
PADUA – NUMBER OF HOPS
With buildings, with junctions

## Slide 35
5
With buildings, without junctions
PADUA – NUMBER OF SLOTS
With buildings, with junctions